## Slide 1: Tinkercad 3D Design & EV Concept Car Workshop
Part 1: Introduction to Tinkercad
& Car Chassis Design

## Slide 2: Session 1: Introduction to Tinkercad
Guess what? Even NASA uses CAD!

## Slide 3
CAD stands for computer-aided design software.
Engineers, architects, artists, and others use CAD to create precise 2D drawings and 3D models.
Notes: Bottom image https://res.cloudinary.com/engineering-com/image/upload/w_640,h_640,c_limit,q_auto,f_auto/bigstock-Female-Engineer-Using-CAD-Syst-98580293_rfhmuh.jpg
Top Image:
https://damassets.autodesk.net/content/dam/autodesk/www/solutions/cad-software/mechanical-engineers-thumb-600x300.jpg
Text Techopedia.com: https://www.techopedia.com/definition/2063/computer-aided-design-cad
Computer-aided design (CAD) is a computer technology that designs a product and documents the design process. CAD may facilitate the manufacturing process by transferring detailed diagrams of a product’s materials, processes, tolerances and dimensions with specific conventions for the product in question. It can be used to produce either two-dimensional or three-dimensional diagrams, which can then when rotated to be viewed from any angle, even from the inside looking out.
CAD is used as follows:
To produce detailed engineering designs through 3-D and 2-D drawings of the physical components of manufactured products.
To create conceptual design, product layout, strength and dynamic analysis of assembly and the manufacturing processes themselves.
To prepare environmental impact reports, in which computer-aided designs are used in photographs to produce a rendering of the appearance when the new structures are built.
CAD systems exist today for all of the major computer platforms, including Windows, Linux, Unix and Mac OS X. The user interface generally centers around a computer mouse, but a pen and digitizing graphic tablet can also be used.
Most U.S. universities no longer require classes for producing hand drawings using protractors and compasses. Instead, there are many classes on different types of CAD software. Because hardware and software costs are decreasing, universities and manufacturers now train students how to use these high-level tools. These tools have also modified design workflows to make them more efficient, lowering these training costs even further.

## Slide 4
3-dimensional orthographic view
2-dimensional isometric view
Notes: Illustration of what 2D and 3D objects look like

## Slide 5: Measuring in 2D
2D objects have a length and width
Notes: Image: https://www.mapeihome.com/calculating-total-area

## Slide 6: Measuring in 3D
3D objects have a length, width, and height
Notes: Image: https://www.quora.com/What-is-the-length-of-a-rectangular-prism-How-is-this-determined

## Slide 7: Spatial Visualization: Looking at objects ALL ways! Isometric (3D) view and Orthographic (2D) view
Notes: Visual Spatialization - or visual-spatial ability is the ability to mentally manipulate 2-dimensional and 3-dimensional figures
When we talk about 2D shapes (orthographic view), we talk about sides and angles.
The angles of a 2D shape are also sometimes referred to as 'vertices' (singular: vertex).
When we talk about 3D shapes (isometric view), we talk about faces, edges and vertices.
The faces are the flat parts of the shape.
The edges are the lines where two faces meet.
The vertices are the points where two or more edges meet.
Rotation - is a motion of a certain space that preserves at least one point
Measured in degrees (90°, 180°, 270°, 360°)
In planes (about axes x, y, z) - right hand rule

## Slide 8: Tinkercad 3D Design

## Slide 9: Tinkercad Tips
Use a USB mouse
Measure in millimeters (mm)
Click on the upper left waffle box icon to return to your project homepage.
Example of Tinkercad project page

## Slide 10: Tinkercad Tips
Combine shapes to create new designs
Make sure shapes are touching
Project is flat on the workplane

## Slide 11: Create Tinkercad.com account
Notes: Teachers & Parents Tinkercad blog:
https://blog.tinkercad.com/tag/teachers-parents

## Slide 12: Student or Personal Tinkercad Account
Notes: Tinkercad K12 resources:
Tinkercad Google Classroom Set-Up: https://www.youtube.com/watch?v=uDFKwGVIKlA
Tinkercad Share to Google Classroom:
https://www.youtube.com/watch?v=__jxETVH0SI
How to get started in Tinkercad in your classroom: https://www.youtube.com/watch?v=XSd_d8FRS0A
Keeping learners engaged for the summer:
https://www.youtube.com/watch?v=m77wB4AQDk0
How to use Tinkercad for PBL:
https://www.youtube.com/watch?v=zKvl-emwt9Y
Tinkercad webinar resources:
https://drive.google.com/drive/folders/1k64jyfG0y8GKQ0ylWpW56vO_aINubKGi

## Slide 13: Tinkercad Tutorials

## Slide 14: Tinkercad Project Page
Click the “waffle box” icon to return to project home page.

## Slide 15: Tinkercad Project Page
Tinkercad resources

## Slide 16: Tinkercad Project Page
Tinkercad applications:
3D Design
Circuits
Codeblocks

## Slide 17: Tinkercad Project Page
Click a Tinkercad application
Create a new design

## Slide 18: Tinkercad Workplane
Default name
Rename project

## Slide 19: Tinkercad Workplane
Change 3D design to
Minecraft block design
Lego block design

## Slide 20: Tinkercad Workplane
Project view options
Right click-rotate
Left click-select, move object

## Slide 21: Tinkercad Workplane
Copy, paste, duplicate, delete objects
Back arrow or ctrl Z to undo
Forward arrow or ctrl Y to redo

## Slide 22: Tinkercad Workplane
Show all
Group
Ungroup
Align
Mirror

## Slide 23: Tinkercad Workplane
Manage 3D files

## Slide 24: Tinkercad Workplane
Add workplane and ruler options

## Slide 25: Tinkercad Workplane
Edit workplane settings

## Slide 26: Tinkercad Shape Interface
3D Design options:
Shapes
Text & numbers
Characters
Connectors

## Slide 27: Tinkercad Shape Interface
Click white “handles” to change object dimensions.

## Slide 28: Tinkercad Shape Interface

## Slide 29: Tinkercad Shape Interface
Left click and drag the top black cone to raise and lower an object.

## Slide 30: Tinkercad Shape Interface
Left click and drag the lower arrows to rotate an object.

## Slide 31: Tinkercad Shape Interface
Left click and drag the upper arrows to tilt an object.

## Slide 32: It’s YOUR turn to get creative with 3D design!
Instructions:
Go to the “3D” tab in Tinkercad
Click “Create New Design”
File name: “EV Concept Car”
Reminders:
Project is flat on the workspace
Objects are touching
Back arrow or “Control Z” to undo
Click on the Tinkercad “waffle box”. icon to get back to your project page
Don’t get frustrated, have fun!

## Slide 33: Session 2: Car Chassis Design
Length: 60 cm
Width: 30 cm
Height: 5 cm
Drag a cube onto your workplane, and change the dimensions.

## Slide 34: More shapes!
Notes: Now we can add wheels! If there isn’t an option to add a wheel, you can click on more shapes to see even more options.

## Slide 35: Add a wheel to your project

## Slide 36: Scale the wheel
Change to 20
Notes: Click on the measurements tool and then click on the wheel.

## Slide 37: Scale the wheel (cont.)
Change to 12
Notes: Click on each measurement to edit the numbers

## Slide 38: Duplicate your first wheel

## Slide 39: Pull it out from the first wheel

## Slide 40: Make an axle
To create an axle, take a new cylinder and rotate it 90°
(click on the 0° and type in 90).

## Slide 41: Make an axle (cont.)
Length = 55 cm
Width = 2 cm
Height = 2 cm
Make it thin
Adjust the dimensions to your liking, you are able to modify this as you work.

## Slide 42: Centering objects
Pull the axle off the ground and try to put it in the center of the two wheels.

## Slide 43: Centering (cont.)
Your design does not have to be perfect yet.
Just make sure the chassis is between the axle and wheels.

## Slide 44: Selecting a group
Hold shift, click on your axle and wheels, all three should be highlighted in blue.

## Slide 45: Align objects
Click on the align tool.

## Slide 46: Align (cont.)
Align the centre two dots, which will align it in the center of this view.
Then view it from the side and align it again.

## Slide 47: Grouping parts
Group the axle and the wheels to prevent them from separating.

## Slide 48: Create more wheels
Duplicate again!

## Slide 49: Changing sizes
If one part is too narrow or too wide, you can always change the dimensions.

## Slide 50: Chassis design
Use the “Align” tool to align the wheels, axles, and chassis.

## Slide 51: Keeping wheels on the road
Place the axle below the chassis.

## Slide 52: Finish the chassis
Group all items together.

## Slide 53: Tinkercad 3D Design & EV Concept Car Workshop
Part 2: Concept Car Body Design & Review

## Slide 54: Session 3: Concept Car Body Design
Get creative!
Choose shapes to combine to form the custom car body (fit within 30cm by 60cm chassis)
Select color(s)
Make “holes” and then group them with a body
Customize the wheels, body shape, etc.
Group objects as you go and on the final draft
design
What shapes work best?

## Slide 55: Session 4: Concept Car Design Review
Take a screenshot of your 3D model EV Dream Car design.
Share it with the class!
What was the best part of creating your design?
What was the most challenging part of creating your design?
How would you change your design next time?

## Slide 56: End of Workshop You CAD do it!